## Slide 1: CO2 emissions of geothermal plants Prof. Rosalind Archer Director – Geothermal Institute

## Slide 2
Image: https://kupu.maori.nz/kupu/He-waka-eke-noa
Translation – We are all in this together

## Slide 3
Image: http://www.espn.com/espn/feature/story/_/id/27583628/understanding-all-blacks-supreme-success

## Slide 4: Is Geothermal Carbon Neutral?
Emissions in g CO2/kWh
Worldwide 122 (average)
Indonesia 42 to 73
Iceland 50 (average) Lignite coal 982.6
California 81.8 (average) Bituminous coal 937.2
Italy 330 (average) Fuel oil 742.6
Turkey 400 to 1640 Natural Gas 552.4
Reference: Layman, Stanford Geothermal Workshop, 2017
Notes: Electricity context. Direct use?

## Slide 5: What’s going on in Turkey?
“Exploited geothermal systems in western Turkey are fault-controlled, moderate temperature (150-240ºC) resources with low to moderate salinity, typically hosted within reservoir rocks dominated by carbonates, marble and calc-schists in addition to quartzites and gneisses (Simsek, 1985; Yilmazer et al., 2010; Ozgur, 2016).
The dissolution of calcite (CaCO3), which is widespread in the carbonate reservoir rocks, due to hydrothermal processes is generally considered the most likely explanation for the high CO2 content in Turkey geothermal reservoirs (Haizlip et al., 2016).”
Reference: Layman, Stanford Geothermal Workshop, 2017

## Slide 6: What about New Zealand?
Image: McLean and Richardson, NZ Geothermal Workshop, 2019

## Slide 7: What about New Zealand?
From: https://nzgeothermal.org.nz/geothermal-energy/emissions/

## Slide 8: Key Considerations
Reference: McLean and Richardson, NZ Geothermal Workshop, 2019
What is the natural state of the system?
How will it change after development?
Rotorua: at least 1000 tCO2/day
Rotokawa: 441 tCO2/day
Crater floor of White Island volcano: 124 tCO2/day

## Slide 9: Key Considerations
Values quoted are operational. What about lifecycle emissions (including construction and decommissioning)?
Are there also methane emissions?
Emissions may decline in time due to degassing.
Reference: McLean and Richardson, NZ Geothermal Workshop, 2019

## Slide 10: New Zealand Emission Reduction
Reference: NZ Ministry of Business, Innovation and Enterprise

## Slide 11: Binary Plants and CO2
Binary plants operate in a closed loop with no atmospheric emissions (if the wells are pumped, as opposed to artesian). However Layman (2017) notes that:
- high gas contents can depress the flash point in wells down to depths below the technical limit of downhole pumps
- reservoir temperatures may exceed the 190ºC temperature limitation of the pumps.
Image: https://cdn.powermag.com/wp-content/uploads/2015/03/PWR_030115_NZGeo_Fig4.jpg

## Slide 12: Geothermal – A Route to Displace Liquid Fuels?
Geothermal energy will be used in a pilot plant in New Zealand (at Mokai) to produce hydrogen, which can be used as a transport fuel.
NZ also incentivising electric vehicles.
http://www.tuaropaki.com/our-business/hydrogen-energy/
https://www.stuff.co.nz/business/101292443/joint-iwi-and-japan-hydrogen-pilot-project-for-taup
Notes: NZ embracing electric vehicles (12,000 in NZ I was number 1,200)

## Slide 13: CarbFix - Iceland
Hellisheidi power plant has pumped carbon dioxide-rich gases emitted by the plant into deep underground basalt formations, mixing them with water and chemically solidifying the carbon dioxide.
Reference: Matter et al., Science, 2016
Image: https://www.scienceabc.com/innovation/
carbon-dioxide-capture-storage-underground-turned-stone-climate-change-global-warming.html
Notes: Atmospheric CO2 can be sequestered by injecting it into basaltic rocks, providing a potentially valuable way to undo some of the damage done by fossil fuel burning. Matter et al. injected CO2 into wells in Iceland that pass through basaltic lavas and hyaloclastites at depths between 400 and 800 m. Most of the injected CO2 was mineralized in less than 2 years. Carbonate minerals are stable, so this approach should avoid the risk of carbon leakage

## Slide 14: Coupled Surface/Reservoir Modelling
Image: Mohammed Dabbour, University of Auckland

## Slide 15: Concluding Remarks
Geothermal systems (in their natural state) and power plants have a variable CO2 emissions profile.
Geothermal in NZ played an important role in decarbonising electricity sector.
CO2 from geothermal power generation may be mitigated by appropriate plant technology, reinjection, displacement of liquid transport fuels etc.

## Slide 16
Prof. Rosalind Archer
r.archer@auckland.ac.nz
@Geothermal_Inst (Twitter)
Rosalind Archer (LinkedIn)